## Slide 1: (U) MATLAB Tools – CFAR Processor
Jeff Hole

## Slide 2: Current Capabilities
1-dimensional CFAR
  Arbitrary number of training cells and guard cells for both sides of the cell-under-test (CUT)
  A signal matrix can be input (NxM) and an argument specifying which dimension to apply the CFAR across
    Utilizes vectorized MATLAB features for fast operation
2-dimensional CFAR
  Arbitrary number of training cells in both dimensions for number of training cells and guard cells.
    Currently limited to centered CUT in both dimensions

## Slide 3: Things To Add/Explore
Independent variance measures on left and right side training cells
  Weight sides differently based on relative magnitude (small feature extraction might perform better)

## Slide 4: Some Mathematical Relationships 2-D CFAR
Total number of cells in CFAR kernel footprint
  Assuming the same number of training and guard cells on each side (symmetrical CFAR footprint)
    # of horizontal training cells (on one side)
    # of horizontal guard cells (on one side)
    # of vertical training cells (on one side)
    # of vertical guard cells (on one side)
+1 is for the cell-under-test, which contributes to the overall footprint area

## Slide 5: Some Mathematical Relationships 2-D CFAR
Total number of cells in CFAR kernel footprint
  Assuming asymmetrical CFAR footprint
    # of horizontal training cells (on right side, left side respectively)
    # of horizontal guard cells
    # of vertical training cells (on one side)
    # of vertical guard cells (on one side)
+1 is for the cell-under-test, which contributes to the overall footprint area

## Slide 6: Edge/Border Cases
The default operation is to calculate the number of active averaging cells at each cell-under-test (CUT).
  This can be accomplished in a single line of code:
    normFactors = conv2(ones(size(signal)), cfar_kernel, ‘same’);
Using this, we can run the one liner:
    cfar = threshold * conv2(signal, cfar_kernel, ‘same’) ./ normFactors;